## Slide 1: P&S Modern SSDs Introduction to MQSim
Rakesh Nadig
Prof. Onur Mutlu
ETH Zürich
Fall 2022
30th November 2022

## Slide 2: Outline
Internal Components of a Modern SSD
Introduction to MQSim
Mechanism
Code structure
Configuring MQSim

## Slide 3: Outline
Internal Components of a Modern SSD
Introduction to MQSIM
Mechanism
Code structure
Configuring MQSim

## Slide 4: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)

## Slide 5: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host (e.g., SATA, NVMe)

## Slide 6: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host (e.g., SATA, NVMe)
  Flash Translation Layer (FTL): manages resources, processes I/O requests

## Slide 7: Internal Components of a Modern SSD
Back End: data storage
  Memory chips (e.g., NAND flash memory, PCM, MRAM, 3D XPoint)
Front End: management and control units
  Host–Interface Logic (HIL): protocol used to communicate with host
  Flash Translation Layer (FTL): manages resources, processes I/O requests
  Flash Channel Controllers (FCCs): sends commands to memory chips, transfers data between the front end and back end

## Slide 8: FTL: Managing the SSD’s Resources
Flash writes can be performed only on pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency

## Slide 9: FTL: Managing the SSD’s Resources
Flash writes can take place only to pages that are erased
  Perform out-of-place updates (i.e., write data to a different, free page), mark old page as invalid
  Update logical-to-physical mapping (makes use of cached mapping table)
  Some time later: garbage collection reclaims invalid physical pages off the critical path of latency
Write cache decreases resource contention, reduces latency

## Slide 10: Outline
Internal Components of a Modern SSD
Introduction to MQSIM
Mechanism
Code structure
Configuring MQSim

## Slide 11: MQSim
Accurately models conventional SATA-based SSDs and modern multi-queue SSDs
  Multi-queue protocols
  Supports steady-state behavior
  with preconditioning
  Models end-to-end I/O request latency
Flexible design
  Modular components
  Ability to support emerging non-volatile memory (NVM) technologies
Open-source release: http://github.com/CMU-SAFARI/MQSim
  Written in C++
  MIT License
Notes: SATA: Native Command Queue

## Slide 12: Support for Multi-Queue Protocols
Conventional host interface (e.g., SATA)
  Originally designed for magnetic hard disk drives: only thousands of IOPS per device
  OS handles scheduling, fairness control for I/O requests
SSD Device
Process 1
Process 2
Process 3
OS Block Layer
Hardware dispatch queue
I/O Scheduler
Software
I/O Request
Queue

## Slide 13: Support for Multi-Queue Protocols
Modern host interface (e.g., NVMe)
  Takes advantage of SSD throughput: enables millions of IOPS per device
  Avoids OS intervention: SSD must perform scheduling, ensure fairness
SSD Device
Process 1
Process 2
Process 3
Hardware
I/O Request
Queue

## Slide 14: High-Performance Steady-State Model
SSDs should be evaluated in steady state
  Fresh, out-of-the-box (FOB) devices are unlikely to perform garbage collection
  Data cache is not warmed up for an FOB device
Many SSD simulators simulate only FOB devices or incorrectly model steady-state behaviour
Difficult to reach steady state in most simulators
  Very slow
  Widely-used traces aren’t large enough for proper warm-up

## Slide 15: Complete Model of Request Latency
< 1µs
50-110µs
20µs
4µs
50-110µs
20µs
< 1µs
< 1µs
< 1µs

## Slide 16: SSD Back End Model
Three major latency components of the SSD back end
  Address and command transfer to the memory chip
  Flash memory read/write execution for different NAND technologies (1-bit, 2-bit and 3-bit per cell)
  Data transfer to/from memory chips
Die- and plane-level parallelism and advanced command execution
Decouples the sizes of read and write operations
  Page-sized write operations
  Sub-page read operations

## Slide 17: SSD Front End Model
Host-Interface Model
  NVMe multi-queue (MQ) and SATA native command queue models for a modern SSD
  Different priority classes for host side request queues as per the NVMe standard specification
Data Cache Manager
  DRAM-based cache with Least Recently Used (LRU) replacement policy to cache recently accessed data
FTL Components
  Address translation unit
  Garbage collection and wear-leveling unit
  Transaction scheduling unit
  Support for multi-flow request processing

## Slide 18: More in the Paper
https://www.usenix.org/system/files/conference/fast18/fast18-tavakkol.pdf

## Slide 19: Outline
Internal Components of a Modern SSD
Introduction to MQSIM
Mechanism
Code structure
Configuring MQSim

## Slide 20: Mechanism
MQSim is a discrete-event based simulator
Each operation performed by MQSim is an event (Command/Address transfer, Read data out etc.)
A red-black (RB) tree maintains the events in the order of their completion times
Each node of the RB tree has a key which indicates the timestamp to finish and, the value is the callback function
For example, at time 5, a data transfer event starts, and the event will execute for another 5 time-units. The simulator will insert a node <5 + 5, callback> into the tree
At each simulation cycle, the simulator will find the node with the smallest time (value), set the timer to that timestamp, execute the callback function
MQSim supports Real disk traces (e.g., MSR Cambridge Block I/O Traces, YCSB etc.) and Synthetic workloads (generated by the simulation engine)

## Slide 21: Initialization
MQSim components (FTL, SSD Device, TSU etc.) are represented as objects and maintained in a map
The objects in the map are iterated through and corresponding functions are executed
Each object maintains their own version of setup_triggers, start_simulation etc.

## Slide 22: Simulation Engine
Engine.cpp/start_simulation
The callback function is Execute_simulator_event

## Slide 23: Mechanism of MQSim
A simulator event is registered using the Register_sim_event function
Example: An event is registered for sending the Read command and address

## Slide 24: Outline
Internal Components of a Modern SSD
Introduction to MQSIM
Mechanism
Code structure
Configuring MQSim

## Slide 25: Code Structure
ssdconfig.xml – configuration file that contains the preferred SSD configuration
workload.xml – workload definition file
traces – folder in which the trace files have to be placed
src/sim – contains the files related to the simulation engine
src/nvm_chip – code related to NVM chip. Contains files for die, plane, block and page
src/ssd – contains files related to Flash Translation Layer and Transaction Scheduling Unit
src/host – files related to trace and synthetic workloads, PCIe etc.

## Slide 26: Code Structure
Code flow
  Host -> Data Cache -> Address Translation Unit -> TSU -> Flash Controller -> NVM_Chip
Some important functions:
  Data Cache Manager: process_new_user_requests()
  Address Mapping Unit: translate_lpa_to_ppa_and_dispatch()
  Transaction Scheduling Unit: Schedule()
  Flash Controller: send_command_to_chip()

## Slide 27: Outline
Internal Components of a Modern SSD
Introduction to MQSIM
Mechanism
Code structure
Configuring MQSim

## Slide 28: SSD Configuration File (ssdconfig.xml)
Host parameters
  PCIe_Lane_Bandwidth: the PCIe bandwidth per lane in GB/s
  PCIe_Lane_Count: the number of PCIe lanes
Device Parameters
  HostInterface_Type: the type of host interface. Range = {NVME, SATA}
  IO_Queue_Depth: the length of the host-side I/O queue.
  Data_Cache_Capacity: the size of the DRAM data cache in bytes
  Ideal_Mapping_Table: if mapping is ideal, all the mapping entries are found in the DRAM and there is no need to read mapping entries from flash
  Transaction_Scheduling_Policy: the transaction scheduling policy that is used in the SSD back end. Range = {OUT_OF_ORDER as defined in the Sprinkler (Jung et.al., HPCA 2014), PRIORITY_OUT_OF_ORDER which implements OUT_OF_ORDER and NVMe priorities}

## Slide 29: SSD Configuration File (ssdconfig.xml)
Device Parameters
  Flash_Channel_Count: the number of flash channels in the SSD back end
  Flash_Channel_Width: the width of each flash channel in bytes
  Chip_No_Per_Channel: the number of flash chips attached to each channel in the SSD back end
NAND Parameters
  Flash_Technology: Range = {SLC, MLC, TLC}.
  Page read latency for LSB, CSB and MSB pages (in nanoseconds)
  Page program latency (in nanoseconds)
  Block_Erase_Latency: erase latency in nanoseconds
  Block_PE_Cycles_Limit: the PE limit of each flash block

## Slide 30: SSD Configuration File (ssdconfig.xml)
NAND Parameters
  Die_No_Per_Chip: the number of dies in each flash chip
  Plane_No_Per_Die: the number of planes in each die
  Block_No_Per_Plane: the number of flash blocks in each plane
  Page_No_Per_Block: the number of physical pages in each flash block
  Page_Capacity: the size of each physical flash page in bytes
  Page_Metadata_Capacity: the size of the metadata area of each physical flash page in bytes

## Slide 31: Trace-based workload configuration

## Slide 32: Synthetic workload configuration

## Slide 33: MQSim Output File

## Slide 34: MQSim usage
Linux
  $ make
  $ ./MQSim -i <SSD Configuration File> -w <Workload Definition File>
Windows
  Open the MQSim.sln solution file in MS Visual Studio 2017 or later.
  Set the Solution Configuration to Release (it is set to Debug by default).
  Compile the solution.
  Run the generated executable file (e.g., MQSim.exe) either in command line mode or by clicking the MS Visual Studio run button. Please specify the paths to the files containing the 1) SSD configurations, and 2) workload definitions.
  $ MQSim.exe -i <SSD Configuration File> -w <Workload Definition File>

## Slide 35: P&S Modern SSDs Introduction to MQSim
Rakesh Nadig
Prof. Onur Mutlu
ETH Zürich
Fall 2022
30th November 2022